## Slide 1: MOC – Myanmar RAMS
Main characteristics
Architecture and components
Three core functions:
Data Display and visualization
ROMDAS Data import, processing and management
Analysis and reporting
21 March 2018

## Slide 2: MRAMS Main characteristics
Objective: Asset Management of ±25 000 miles of MOC managed roads
Focus on Data integration, GIS and Thematic Asset Mapping, query and reporting
Free solution: fully open source / central open relational database / source code available
Integrates ROMDAS / Roadroid / OSM / MIMU Data/ Google Maps
Simulates LRS and Dynamic segmentation
For basic (sporadic) and advanced (almost daily) users

## Slide 3: MRAMS System Architecture

## Slide 4: MRAMS Components

## Slide 5: Data Display and visualization

## Slide 6: Connect to MRAMS and Load Layers
All data on central server, or local computer. Relational Geodatabase format.

## Slide 7: Map Background services
Access to background maps from Google, Bing, Open Street Map etc..

## Slide 8: Map templates
These are predefined maps which allow quickly building customized maps at various scales.

## Slide 9: ROMDAS Data import, processing and management

## Slide 10: ROMDAS Data Import and processing.
After data collection, validate data and ensure QC via ROMDAS DataView Software
Optionally, use DataView to add data extracted from Video analysis
Import ROMDAS network and IRI related information into RAMS
Import Asset details into RAMS
Process data to insert in valid MOC Road Network GIS

## Slide 11: ROMDAS DataView – Quality Control Linking with MRAMS

## Slide 12: Analysis

## Slide 13: Road Attribute Mapping
Create Road Layer maps using color scheme or line width.

## Slide 14: Database & spatial queries - Reporting
Any spatial and or attribute query with export report as PDF / HTML or CSV-Excel. This example shows average IRI by State, exported to Excel for further analysis.

## Slide 15: Routing
Shortest route calculation between two points in the network.

## Slide 16: QGIS Spatial analysis
Standard QGIS functionality (overlay, buffering, intersection, clipping… ) to link road quality data with any other spatial data for:
planning purposes
budgeting
Monitoring
Based on standard QGIS functions: to be designed and documented

## Slide 17: Conclusion

## Slide 18: Planning & Future Implementation
Installation MRAMS and Training (Q2/2018, TBC) incl. DataView
Master “MOC Road layer” and identification system
Define Planning and logistics of of ROMDAS data collection by State
Further functional design required for specific needs of MOC regarding RAMS
Use of ROMDAS DataView in combination with QGIS/MRAMS (QA/QC)
RAMS / GIS Lab – making it operational and promote GIS activities with high quality A1-color maps for different divisions (design…)

## Slide 19: Thank you!